## Slide 1: Connected Autonomous Vehicles
David Schultens,
2023 March 31 T07:20 & 21:20 UTC
David@OpenVideoSystem.com

## Slide 2: Connected Autonomous Vehicles (CAV)
Collaboratively and constantly refined AI Models
  Comparison of results in Simulation of Use Cases.
  Partitioning of AIM component revisions
  Improved interfaces and Licensed Framework Reference from MPAI
Users/regulators: make sure that a CAV is safe, reliable, and explainable.
Facilitated by CAV’s componentization for Edge compute.
Standard-based components accelerate a CAV mass market.
CAV standards as milestones in a process for intercommunication,
moving from research to standardization to deployment.

## Slide 3: MPAI approach to standardisation
MPAI-AIF enables independently sourced AI Modules having standardised interfaces to be executed in an environment with standardised APIs.
User Agent
Communication
Global Storage
Controller
MPAI Store
AI Workflow (AIW)
AIM
Storage
Access
Inputs
Outputs
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
Open market of
components with
standardises
functions and
Interfaces,
competing in
performance.

## Slide 4: Connected Autonomous Vehicles (CAV)
Collaboratively and constantly refined AI Models
  Comparison of results in Simulation of Use Cases.
  Partitioning of AIM component revisions
  Improved interfaces and Licensed Framework Reference from MPAI
Users/regulators: make sure that a CAV is safe, reliable, and explainable.
Facilitated by CAV’s componentization for Edge compute.
Standard-based components accelerate a CAV mass market.
CAV standards as milestones in a process for intercommunication,
moving from research to standardization to deployment.

## Slide 5: Elements of a CAV Use Case Simulation
Passenger
Roadside Unit
Traffic light
Human
Other vehicles
CAV-enabled vehicles

## Slide 6: CAV Subsystems containing AIM (modules)
Environment Sensing Subsystem
(ESS)
Human-CAV Interaction
(HCI)
Autonomous Motion Subsystem (AMS)
Motion Actuation Subsystem
(MAS)
3-Apr-23
6

## Slide 7: Functions of CAV subsystems
Human-CAV interaction (HCI) responds to hum­ans’ commands and queries, sensing activ­ities during travel, activates other sub­systems required by:
  Humans as deemed nec­essary.
  Environment by identified conditions.
Environment Sensing Subsystem (ESS) acquires in­formation from the environment
Synthesis of sensor data creates and shares
Basic Environment Representation (BER).
Autonomous Motion Subsystem (AMS) builds a Full Environment Representation (FER) using internal and external edge compute (BERs from other CAVs and RSU) information to automatically route plan safely avoiding collision and efficiently flocking together.
Motion Actuation Subsystem (MAS) senses information from and
Actuates motion instructions in the physical environment and sends feedback.

## Slide 8: HCI Human CAV Interaction
S
Personal Status Extraction
Speech Recognition
Language Understanding
Face Object
Human Object
Recognised
Text
Speech
Speech
Speech
Audio Scene Description
Physical Object Identification
Physical Object
Face Object
Face Recognition
Meaning
Text (Lang-Und)
Personal Status
Face ID
Environment Sensing Subsystem
Audio
(Outdoor)
Audio
(Indoor)
Text
Dialogue Processing
User Agent
Communication
Controller
Global Storage
MPAI Store
Speaker Recognition
Speaker ID
Physical Object ID
Autonomous Motion Subsystem
Command
Response
Output Text
Personal Status Display
Machine
Gesture
Machine
Face
Machine
Speech
Machine
Text
Output
Personal Status
Text
Recognised Text
Personal Status
Visual Scene Description
Video
(Outdoor)
Autonomous Motion
Subsystem
Full Envron..
Representation
Viewer
Full Environment Representation
FWR Audio
FER Commands
FWR Video
Human Object
Video
(Outdoor)

## Slide 9
Traff.Sig. Recognition
C. Scene Description
Offline Map Data
Radar Data
Lidar Data
Ultrasound Data
Audio Data
L. Scene Description
R. Scene Description
U. Scene Description
M. Scene Description
Spatial Attitude Generator
GNSS Data
A. Scene Description
Motion Actuation Subsystem
Autonomous Motion Subsystem
Basic
Environ. Represent.
Other Environment Data
Spatial Attitude
Controller
MPAI Store
User Agent
ESS Data Fusion
Radar Scene D.
Radar Scene D.
Road Topology
Camera Scene D.
Map Scene D.
Audio Scene D.
BER
BER
Camera Data
Camera Data
Spatial Attitude
BER
BER
BER
BER
BER
Ultrasound Scene
Spatial
Attitude
Microphone
Array Geom.

## Slide 10
Route Planner
Path Planner
Route
Motion Planner
Obstacle Avoider
Command Issuer
Full Environment Representation (FER) Fusion
Environment Sensing Subsystem
Human-CAV Interaction
Decision Recorder
Basic Environment
Representation
Full Environment
Representation
FER
FER
FER
FER
Destination
User Agent
Route
Path
Trajectory
Trajectory
Command
Feedback
FeedBack
Feed
back
Controller
Communication
MPAI Store
Global Storage
Basic Environment
Representation
Other V2X Data
Full Environment
Representation
Motion Actuation Subsystem
Environment Sensing Subsystem
Alert
Offline Map
R. State
R. State
R. State
R. State
Trajec--tory
Path
Trajec--tory
Env.
Info.

## Slide 11
Autonomous Motion Subsystem
(AMS)
Motion
Communication
Global Storage
Road wheel motor
Road wheel direction
Brakes
Odometer
Accelerometer
Speedometer
Other Environment Data
Environment Sensing Subsystem (ESS)
Command Interpreter
Commands
Feedback
Controller
Spatial Attitude Generation
MPAI Store
Spatial
Attitude
User Agent

## Slide 12: Plans/1
MPAI is developing Technical Report – Architecture of Connected Autonomous Vehicles (MPAI-CAV) defining 4 interconnected subsystems that:
Understands human utterances (HCI).
Plans a Route to reach a destination.
Senses and builds a representation of the external Environment (BER).
Exchanges BER with other CAVs and CAV-aware entities.
Makes decisions about how to execute the Route (AMS).
Actuates the motion (MAS).

## Slide 13: Plans/2
For each Subsystem, the Technical Report provides:
The Function of the Subsystem.
The Functional Requirements of some I/O data.
The Topology of the Components (AI Modules).
For each Subsystem Component (AI Module) the Technical Report provides :
The Function of the AIM
The Functional Requirements of some I/O data.
The Formats of some I/O data.

## Slide 14
Join MPAI
Share the fun
Build the future!
https://mpai.community/
We look forward to your
participation in this
exciting project!