## Slide 1: Neural Network Watermarking
.
2023/12/12 T15:00UTC
http://nnw.mpai.community

## Slide 2: Neural Networks today
Deployed in an increasing variety of domains
Continuously renewed (industry & academia)
At the heart of various autonomous systems:
  Autonomous robots
  Unmanned vehicles
Deployed in more and more critical domains:
  Medical decisions
  Autonomous vehicles with passengers

## Slide 3: Why watermarking is useful for Neural Networks
Machine learning is a costly field:
  Buying AI solution ranges from $ 6000 to $300.000
  Renting a pre-built module costs around $ 40.000/year
An AI solution could:
  use multiple alternative Neural Networks to provide an inference -> identifying the one that actually produced the inference is important
  be shared among multiple users -> keeping track of this process is useful
  be altered or maliciously attacked -> identifying such modifications avoid faulty functioning
Ensuring traceability and integrity of Neural Networks becomes mandatory

## Slide 4: Neural Network Watermarking synopsis
Watermarking provides tools allowing to imperceptibly and persistently insert some data into original content
Watermarking Neural Network is a new challenge:
  Watermark insertion is not static (as it was for media) but dynamic, as the watermark can also be:
    inserted during training
    detected from inference
  Evaluation of watermark impact on inference is much more complex than on multimedia quality
Watermarking
Robustness
Imperceptibility
Data payload

## Slide 5: Neural Network Watermarking use cases
Identify an NN
  The retrieved data conveys information about the NN itself.
Identify the actors of an NN
  The retrieved data conveys information about some or all the actors.
Verify the integrity of an NN
  The retrieved data conveys information about NN integrity.
modification
Integrity
checker
output
Detector
input
NN - 007
MPAI
property

## Slide 6: Scope of the MPAI-NNW Standard
MPAI-NNW specifies methodologies to evaluate the following aspects of a neural network watermarking technology:
The impact on the performance of a watermarked neural network and/or on its inference.
How well a neural network watermarking detector/decoder can detect/decode a payload when the watermarked neural network has been modified.
The computational cost of injecting, detecting or decoding a payload in the watermarked neural network.
s
MPAI Tester
Watermark provider
detector
decoder
injector
detector
decoder
injector
NNW - Evaluate performances of watermarking NN
0 1 0 0 0 1 1
Trained NN
Watermarked NN
Modification of performance induced by the watermarking process
Processing cost of the insertion
Processing cost of the detection/decoding phase
detector
No
Yes
0 1 0 0 0 1 1
Performance criteria for the detector/decoder
decoder

## Slide 7: MPAI-NNW Reference software
The purposes of MPAI-NNW Reference software is
  to provide an instance of MPAI-NNW Software for the image classification task
  to upgrade conventional AI-based processing workflows with traceability and integrity checking functions
Two key software components
MPAI User
start
Property Evaluation
end
Inputs
injector
decoder

## Slide 8: MPAI-NNW Reference software: Imperceptibility evaluation
start
end
Training dataset
Embedder
Imperceptibility Evaluation
Testing dataset
Injector “Uchida et al.” method
“0” type
“CIFAR 10” training dataset
“CIFAR 10” testing dataset
injector
0 1 0 0 0 1 1 1
Trained NN
Watermarked NN

## Slide 9: MPAI-NNW Reference software: Robustness evaluation
start
end
Modifications
Robustness Evaluation
Modification ID
Parameters
Decoder “Uchida et al.” method
“4” type
Quantizing
Detector/
Decoder
Test dataset
detector
No
Yes
0 1 0 0 0 1 1 1
decoder

## Slide 10: MPAI-NNW Reference software: Computational cost evaluation
start
end
Memory_footprint
Time_module
Processing cost of the insertion
Processing cost of the detection/decoding phase

## Slide 11: MPAI-NNW Reference software: Upgrading convention MPAI workflows with watermarking functionalities
Example: End-user use-case “Question Answering AIM”
  Buy a “Question Answering” solution
  Make sure about the authenticity of the inference produced by that AIM:
      IPR protection
      No counter fighting
      No malicious (adversial) tempering
End-user
Watermarked NN
Certification of the AI solution
What city is this?

## Slide 12: MPAI-NNW Reference software: Upgrading convention MPAI workflows with watermarking functionalities
Main novelty of MPAI-NNW RS v1.1
  Python-based MPAI AIF implementation
    AIMs represented as Python classes with attributes being the ports and a “run” function
    Controller and User Agent built as server/client program
    JSON AIM/AIW metadata parsed in fully automatized manner for standard topologies (written from top to bottom and left to right)
    Hooks for C code are provided
JSON & AIMs
Controller.py
Input.py
APIs.py

## Slide 13: MPAI-NNW Reference software: Upgrading convention MPAI workflows with watermarking functionalities
*getparse command asks for a .zip folder containing the AIMs and the JSON
Main novelty of MPAI-NNW RS v1.1
  Python-based MPAI AIF implementation
    AIMs represented as Python classes with attributes being the ports and a “run” function
    Controller and User Agent built as server/client program

## Slide 14: MPAI-NNW Reference software: Upgrading convention MPAI workflows with watermarking functionalities
Main novelty of MPAI-NNW RS v1.1
  Python-based MPAI AIF implementation
    AIMs represented as Python classes with attributes being the ports and a “run” function
    Controller and User Agent built as server/client program
    JSON AIM/AIW metadata parsed in fully automatized manner for standard topologies (written from top to bottom and left to right)

## Slide 15: MPAI-NNW Reference software: Upgrading convention MPAI workflows with watermarking functionalities
Main novelty of MPAI-NNW RS v1.1
  Python-based MPAI AIF implementation
  Achieves inference authentication through NNW
Answer
Singapore
Authenticity proof:
True

## Slide 16: Next steps
Develop a set of API to facilitate use of MPAI-NNW Reference Software
Apply the MPAI-NNW Reference Software for other MPAI use cases
The MPAI-NNW Standard is an IEEE Standard (3304)

## Slide 17
https://www.mpai.community/
https://mpai.community/how-to-join/
http://nnw.mpai.community/
MPAI-NNW RS available at:
https://experts.mpai.community/software/mpai-nnw
17
17
17
17
Join MPAI
Share the fun
Build the future

## Slide 18
https://www.mpai.community/
more about NNW at http://nnw.mpai.community/
Join MPAI
Share the fun,
Build the future!
https://mpai.community/how-to-join/