## Slide 1: An introduction to Moving Picture, Audio, and Data Coding by Artificial Intelligence (MPAI)
.
Leonardo Chiariglione – President and Chairman of the Board, MPAI

## Slide 2: MPAI at-a-glance
Who we are |  |  |  | 
Mission | Procedures | Method | Patents | Organisation
Approved Standards |  | 
Ecosystem governance | Execution of AI apps | CAV – Architecture
CAV – Technologies | Audio enhancement | Company performance prediction
Human-Machine Communication | Multimodal conversation | Metaverse – Architecture
Metaverse – Technologies | Neural Ntwk Watermarking | Objects and scenes
Portable avatars | AI Module Profiles | Data Types, Formats & Attributes
Being developed |  | 
AI for Health | Online Gaming | XR Venues
About to start |  | 
Six Degrees of Freedom Audio | Up-sampling Fiter for Video | End-to-End Video Coding

## Slide 3: Who we are

## Slide 4: MPAI: what it is
International, unaffiliated, non-profit SDO.
Develops AI-based data coding standards.
With clear Intellectual Property Rights licensing frameworks.
MPAI: what it does
MPAI: how it does it

## Slide 5: Explainable standards
AI module (AIM)
Speech analysis
Text
Access
Identity
Speech
AI Workflow (AIW)
AI Module AIM
AI Module AIM
AI Module AIM
AI Module (AIM)
Inputs
Outputs
AIM
Storage

## Slide 6: Accessible & timely available standards
After the development, Members holding IP in the standard select the preferred patent pool administrator.
Before initiating a standard, Active Principal Members develop & adopt its Framework Licence (FWL), a licence without values: $, %, dates etc. declaring that the eventual licence will be issued
Not after products are on the market.
At a price comparable with similar standard technologies.
During the development, any Member making a contribution declares it will make its licence available according to the FWL.
12/26/2024
6
Read the MPAI Patent Policy

## Slide 7
Rigorous standards development process
Call for
Technologies
Standard
Development
Community
Comments
Use Cases
Functional
Requirements
Commercial
Requirements
All
Principal Members
Stage 0
Stage 1
Stage 2
Stage 3
Interest
Collection
Proposal
All Members
Stage 5
Stage 4
All
Stage 6
7
Technical
Specification
Principal Members
Reference
Software
Reference
Software
Conformance
Testing
Performance
Assessment
Stage 7

## Slide 8: The MPAI organisation
General Assembly
Requirements Standing Committee
Standing Committees
Board of Directors
Secretariat
Membership& Nominating
Finance & Audit
IPR Support
Industry & Standards
Communication
Development Committees
MMC-DC
GME-DC
AIF-DC
NNW-DC
AIH-DC
CAE-DC
CUI-DC
PAF-DC
XRV-DC
MMM
HMC
CAV
SPG
EVC
EEV

## Slide 9: Approved standards

## Slide 10: MPAI standards, so far
Standard Name | Acronym | TS | RS | CT | PA
Governance of the MPAI Ecosystem | MPAI-GME | 1.1 | 1.0 |  | 
AI Framework | MPAI-AIF | 2.1 | 1.0 |  | 
Compression and Understanding of Financial Data | MPAI-CUI | 1.1 | 1.0 | 1.0 | 1.0
Context-Based Audio Enhancement | MPAI-CAE | 2.3 | 1.4 | 1.4 | 
Connected Autonomous Vehicle | MPAI-CAV | 1.0 |  |  | 
Human and Machine Communication | MPAI-HMC | 2.0 |  |  | 
Multimodal Conversation | MPAI-MMC | 2.3 |  |  | 
MPAI Metaverse Model | MPAI-MMM | 1.2 |  |  | 
Neural Network Traceability | MPAI-NNT | 1.0 |  |  | 
Neural Network Watermarking | MPAI-NNW | 1.0 | 1.2 |  | 
Object and Scene Description | MPAI-OSD | 1.2 |  |  | 
Portable Avatar Format | MPAI-PAF | 1.3 |  |  | 
AI Module Profiles | MPAI-PAF | 1.0 |  |  | 
Data Types, Formats, and Attributes | MPAI-TFA | 1.2 |  |  | 
12/26/2024
10

## Slide 11: Governance of the MPAI Ecosystem (MPAI-GME) V1.1
Technical Specification: Governance of the MPAI Ecosystem sets the rules governing the MPAI Ecosystem:
1 - MPAI 2 – Implementers 3 - MPAI Store 4 - Performance Assessors 5 - Users
The MPAI Store has been established in Scotland as a Company Limited by Guarantee – independent from MPAI.
Some of the roles of the MPAI Store:
  Managing the “Implementer ID” Registration Authority (also for implementations of IEEE versions of MPAI standards).
  Verifying Security, Testing Conformance, and posting Implementations for download.
Performance Assessors are appointed by but independent of MPAI
Read more about MPAI-GME. Download the MPAI-GME standard.

## Slide 12: The MPAI ecosystem
Develops Implem-entations
Assesses Perfor-mance
Verifies security
Tests Conformance
Checks Performance
Implementation
Implementation
OK
OK
Store
Implementer
Performance Assessor
Down-loads Implem-entation
End User
Experience
Score
Implementation
Standards (TS-RS-CT-PA)
MPAI
Conformance Testing
Performance Assessment
Technical Specification

## Slide 13: AI Framework (MPAI-AIF) V2.1
Standard AI Framework enabling dynamic configuration, initialisation, and control of mixed AI and data processing workflows.
Hierarchical structure:
  AI Framework (AIF)
    AI Workflows (AIW)
      AI Modules (AIM).
AIWs may be proprietary or standard, i.e., with standard functions and interfaces, with an explicit computing workflow.
AIMs are specified by their function and interfaces not by their internals.
AIMs can be implemented in hardware, software, hybrid hardware/software.

## Slide 14: AI Framework (MPAI-AIF) V2.1
User Agent
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
Controller (Non-secure/Secure)
Global Storage
MPAI Store
Access
Inputs
Outputs
SAL
Communi-cation
Attestation Service
Encryption Service
Communication Service
AIM/AIW Storage
(non-secure)
AIM/AIW Storage
(secure)

## Slide 15: Context-based Audio Enhancement (MPAI-CAE) V2.3
Improves the user experience for audio applications – teleconferencing, post-production, restoration – in different contexts – in the home, in the studio, etc.
Technical Specification includes:
  4 Use cases: Emotion Enhanced Speech, Audio Recording Preservation, Speech Restoration System, and Enhanced Audioconference Experience (and Reference Software).
  1 Composite AIM: Audio Scene Description
  Data Types.
Reference software.
Conformance Testing.

## Slide 16: Audio Recording Preservation (CAE-ARP)
Packager
A. Irreg. File
Irr. Audio File
Irreg. Images
Irregularity
Images
Audio Analyser
Communication
Global Storage
Video Analyser
A. Irreg. File
V. Irreg. File
Tape Irregularity Classification
Tape Audio Restoration
A. Irreg. File
Irreg. File
Preservation
Audio File
Preservation Audio-Visual File
Preservation
Master Files
Access Copy
Files
Restored
Audio Files
V. Irreg. File
Controller
MPAI Store
User Agent
Editing
List
V. Irreg. File

## Slide 17: Audio Scene Description (Composite AIM)
Audio Analysis Transform
Audio Source Localisation
Audio Separation and Enhancement
Audio Synthesis Transform
Audio Object
Audio Scene
Descriptors
Audio Object (Transform)
Spatial Attitudes
Enhanced Audio Objects (Transform)
Enhanced Audio Objects
Audio Scene Geometry
Audio Descriptors Multiplexing
Space-Time
Audio Scene Descriptors
Audio Object (Transform)

## Slide 18: MPAI-CAE – Six Degrees Audio (CAE-6DF)
Project targeting digital representations of acoustical scenes and other synthetic Audio Objects for rendering arbitrary user- selected points of the audio scene in a perceptually veridical fashion.
capture audio space
audio scene
Computing Platform
Audio Space
Audio Scene
Audio Scene
Audio Scene
Audio Scene
rendering audio space
audio scene
audio scene
audio scene

## Slide 19: Connected Autonomous Vehicle – Architecture (MPAI-CAV) V1.1
Technical Specification: Connected Autonomous Vehicle (MPAI-CAV) – Architecture V1.0 specifies the Architecture of a CAV based on a Reference Model comprising:
A CAV broken down into Subsystems for each of which the following is specified:
  Functions
  Input/output Data
  Topology of Components
Each Subsystem broken down into Components of which the following is specified:
  Functions
  Input/output Data.
Subsystems/Components are assumed to be implemented as AIWs/AIMs.

## Slide 20: MPAI-CAV – Architecture Reference Model
Environment Sensing Subsystem
(ESS)
Human-CAV Interaction
(HCI)
Autonomous Motion Subsystem (AMS)
Motion Actuation Subsystem
(MAS)

## Slide 21: Environment Sensing Subsystem
OfflineMap Scene Description
Ultrasound Scene Description
LiDAR Scene Description
RADAR Scene Description
Visual Scene Description
Spatial Attitude Generation
Audio Scene Description
Autonomous Motion Subsystem
Basic Env. Descriprors
Alert
Motion Actuation Subsystem
Spatial Attitude
GNSS Object
Spatial
Attitude
Audio Object
Audio Scene Descriptors
Alert
Basic Environment Descriptors
Visual Scene Descriptors
Alert
Basic Environment Descriptors
RADAR Scene Descriptors
Alert
Basic Environment Descriptors
LiDAR Scene Descriptors
Alert
Basic Environment Descriptors
Ultrasound Scene Descriptors
Alert
Basic Environment Descriptors
Offline Map Scene Descriptors
Weather Data
Visual Object
RADAR Object
LiDAR Object
Ultrasound Object
Offline Map Object
Controller
Global Storage
Access
Communi-cation
Attestation
Service
Encryption
Service
Communication
Service
MPAI Store
Alert
Alert
Alert
Alert
Basic Environment Description

## Slide 22: MPAI-CAV – Autonomous Motion Subsystem
Route Selection Planner
Path Selection Planner
Route
Motion Selection Planner
Traffic Obstacle Avoider
FED
FED
FED
FED
Route
Path
Trajectory
Trajectory
Road
State
Road
State
Road
State
Road
State
Trajectory
Path
Trajectory
AMS Decision Recorder
Human-CAV Interaction
Basic
Environment
Descriptors
HCI-AMS
Message
AMS-HCI
Message
User Agent
Controller
Global Storage
Access
Communi-cation
Attestation
Service
Encryption
Service
Communication
Service
MPAI Store
Full Environment Description
Environment Sensing Subsystem
Remote AMSs
AMS-MAS msg
Alert
Full
Environment
Descriptors
File
AMS Command Issuer
MAS-AMS msg
Road State
AMS-MAS msg
MAS-AMS msg
Motion Actuation Subsystem
Environment Sensing Subsystem

## Slide 23: Connected Autonomous Vehicles (MPAI-CAV) – Technologies V1.0
To execute its mission, a CAV uses a range of sensors to create a digital twin of the environment it traverses.
MPAI-CAV represents the environment’s digital twin with a Data Type called Basic Environment Descriptors (CAV-BED).
CAV-BED includes:
  Audio-Visual Scene Descriptors (OSD-AVS).
  CAV-specific data, e.g., Other Environment Data (humidity, etc.) and Road State.
A CAV exchanges portions of its BED with other CAVs in range.
Therefore, the CAV produces Full Environment Descriptors, yet another OSD-AVS environment representation integrated by other CAV-specific data.

## Slide 24: CAV Data Types
HCI | AMS-HCI Message | Audio Basic Scene Descriptors | Audio Object | Audio Scene Descriptors | 
 | AV Basic Scene Descriptors | Audio-Visual Object | AV Scene Descriptors | Body Descriptors | 
 | Ego-Remote HCI Message | Face Descriptors | Instance Identifier | Meaning | 
 | Personal Preferences | Personal Profile | Personal Status | Point of View | 
 | Portable Avatar | Selector | Speech Basic Scene Descriptors | Speech Object | 
 | Speech Scene Descriptors | Text Object | Visual Basic Scene Descriptors | Visual Object | 
 | Visual Scene Descriptors |  |  |  | 
ESS | Alert | Basic Environment Descriptors | GNSS Object | LiDAR Basic Scene Descriptors | 
 | LiDAR Object | LiDAR Scene Descriptors | Offline Map Object | Offline Map Scene Descriptors | 
 | Orientation | Path | Position | RADAR Basic Scene Descriptors | 
 | RADAR Object | RADAR Scene Descriptors | Road State | Route | 
 | Space-Time | Spatial Attitude | Traffic Rules | Traffic Sign Annotation | 
 | Trajectory | Ultrasound Basic Scene Descriptors | Ultrasound Object | Ultrasound Scene Descriptors | 
AMS | AMS-MAS Message | AMS Recording Data | CAV Identifier | CAV State | 
 | Ego-Remote AMS Message | Full Environment Descriptors | Road Topology |  | 
MAS | Brake Command | Brake Response | Motor Command | Motor Response | 
 | Spatial Data | Weather Data | Wheel Command | Wheel Response | 

## Slide 25: The «AI-based Compression and Understanding of Industrial Data» standard Company Performance Prediction
Predicts the performance of a company in a time horizon based on:
  Financial risks
  Vertical risks (i.e., seismic and cyber)
  Governance data.
Performance is Default probability, Discontinuity probability. Organisational Index
Compression and Understanding of Financial Data (MPAI-CUI) V1.1
MPAI has issued a Call for MPAI-CUI V2.0 Call for Technologies. The new version will provide non only index and probabilities but also descriptors.
Notes:   Processo che ha portato allo std: UC-FR-FWL-CfT-CC-Std
  I moduli, la loro funzione, in part. Prediction, significato del training e dell’affidabilità dei dati di input
  What comes next (altri rischi)
Applications of CUI-CPP
  Banca, assicurazione, ente pubblico

## Slide 26: MPAI-CUI V1.1 – Reference Model
Controller
Communication
Global Storage
MPAI Store
Governance Data Assessment
Risk Matrix
Financial Data Assessment
Risk Matrix Generation
Organisational
Model Index
Default Probability
Business
Discontinuity Probability
Prediction Result Perturbation
Default Probability
Governance
Risk
Assessment
Financial Statement
Governance Features
Financial Features
Prediction
Horizon
User Agent
Discontinuity and Default Prediction

## Slide 27: Human and Machine Communication (MPAI-HMC) V2.0
Enables new forms of communication between communicating participants called Entities:
  humans present in a real space or represented in a Virtual Space, or
  Machines represented in a Virtual Space or rendered in a real space as speaking avatars.
Entities acts in a Context using text, speech, face, gesture embedded is audio-visual scenes.

## Slide 28
#1
Real scene or representation
in a Virtual Scene
Virtual Scene
#2
Real or virtual scene
#4
Machine
In a Virtual Scene or
rendered as a real scene
Virtual Scene
#3

## Slide 29: MPAI-HMC Reference Model
Input
Visual
Audio-Visual Scene Description
Input
Selector
AV Scene Integration & Description
Input Portable
Avatar
AV Scene
Descriptors
Entity and Context Understanding
Meaning
Machine
Text Obj.
Machine Avatar ID
Output
Portable
Avatar
Output Audio
Audio-Visual Scene Rendering
Input
Text
Controller
Global Storage
MPAI Store
Access
Communication
Attestation Service
Encryption Service
Communication Service
AV Scene
Descriptors
User Agent
Output Portable
Avatar
Output Visual
Input
Audio
Personal
Status
Meaning
Text Object
Entity ID
Instance ID
AV Scene
Geometry
Machine Personal Status
Machine Text Obj.
Entity Dialogue Processing
Text-to-Text Translation
Machine
Translated Text Obj.
Personal Status Display
Output Text
Output Speech

## Slide 30: Multimodal Conversation (MPAI-MMC) V2.3
Technical Specification: Multimodal Conversation (MPAI-MMC) V2 specifies:
Data Formats for analysis of text, speech, and other non-verbal components as used in human-machine and machine-machine conversation applications.
Use Cases implemented in the AI Framework
  Using Data Formats from MPAI-MMC and other MPAI standards.
  Providing recognised applications in the Multimodal Conversation domain.
MPAI-MMC V2 includes
Seven use cases (Conversation with Emotion, Human-CAV Interaction,…)
One composite AIM (i.e., an AIM that includes AIMs)
Several Data Types (i.e., standard data formats).

## Slide 31
Aut. Speech Recognition
Face Descriptors
Body Descriptors
Speech Object
Speech
Object
Speech Object
Face Object
Face ID Recognition
Face ID
Entity Dialogue Processing
Speaker ID Recognition
Speaker ID
Machine Text
Personal Status Display
Machine
Personal Status
Recognised Text
Personal Status
Visual Object Identification
NLU Text
User Agent
Autonomous Motion
Subsystem
Point of View
Machine Portable
Avatar
Meaning
Controller
Global Storage
Access
Communi-cation
Attestation Service
Encryption Service
Communication Service
MPAI Store
Environment Sensing Subsystem
Participant IDs
Meaning
Input Visual
AV Scene Descriptors
Audio=-Visual Scene Rendering
Output Text
AV Scene Descriptors
Visual Object ID
Natural Language Understanding
Visual Scene
Descriptors
Output Visual
Output Audio
Autonomous Motion Subsystem
AMS-HCI
Message
Remote HCIs
Ego-Remote HCI Message
Input Audio
Input Text
Participant
IDs
Visual Scene Descriptors
Visual
Object ID
Personal Status Extraction
View Selector
Speech Scene Geometry
Visual Scene Geometry
Output Speech
Audio-Visual Scene Description

## Slide 32: Virtual Meeting Secretary
S
Natural Language Understanding
Meaning
Input Personal Status
Entity Dialogue Processing
Meaning
Edited
Summary
Input Text
Input
Personal Status
Summary
User Agent
Refined Text
VS Text
VS Personal Status
Personal Status Extraction
Recognised Text
Input Speech
Summary
Body Descriptors
Personal Status Display
Portable Avatar Demultiplexing
Face Descriptors
Input Text
Portable
Avatars
VS Portable Avatar
Automatic Speech Recognition
Meaning
Refined Text
Avatar ID
Avatar ID
Summary Creation Module
VS Avatar Model
Input Speech
Controller
Global Storage
MPAI Store
Access
Communi-cation
Attestation Service
Encryption Service
Communication Service

## Slide 33: MPAI Metaverse Model (MPAI-MMM) – Architecture V1.1
Specifies:
  Operation Model
  Functional Requirements of Processes, Actions, Items, and Basic Data.
Enables metaverse instances (M-Instances) to interoperate if they:
  Rely on the Operation Model
  Use the same Profile
  Use either
    The same technologies, or
    Independent technologies and access Conversion Services transforming M-InstanceA Data M-InstanceB Data.

## Slide 34
human1
User2.1
User1.1
Device2.1
Device3.1
Device1.1
human2
Device2.2
Service1
Service3
User2.2
Service2
M-Instance
Persona2.1.1
Persona2.1.2
Persona1.1.1
object1
Item1.2
human3
Item3.1
Persona2.2.1
Item1.1
User1.1
User3.1

## Slide 35: Functional Requirements of Actions
  Functional Requirements
    Apps Devices
    Services Users
  MMM Scripting Language
  Functional Profiles
MPAI-MMM – Architecture specifies
1 General Actions | 2 Call a Service | 3 Metaverse to Metaverse | 4 Metaverse to Universe | 5 Universe to Metaverse
1.1 Register | 2.1 Author | 3.1 MM-Add | 4.1 MU-Actuate | 5.1 UM-Animate.
1.2 Change | 2.2 Discover | 3.2 MM-Animate | 4.2 MU-Render | 5.2 UM-Capture.
1.3 Hide | 2.3 Inform | 3.3 MM-Disable | 4.3 MU-Send | 5.3 UM-Render
1.4 Authenticate | 2.4 Interpret | 3.4 MM-Embed | 4.4 Track | 5.4 UM-Send
1.5 Identify | 2.5 Post | 3.5 MM-Enable |  | 
1.6 Modify | 2.6 Transact | 3.6 MM-Send |  | 
1.7 Validate | 2.7 Convert |  |  | 
1.8 Execute | 2.8 Resolve |  |  | 
  Operation Model
  Functionalities

## Slide 36: MPAI-MMM – Technologies (MMM-TEC)
General | Process Interaction | Perception | Space
Contract | Message | Audio Object | Basic M-Location
E-Capabilities | P-Capabilities | Audio Basic Scene Descriptors | M-Location
Identifier | Process Action | Audio Scene Descriptors | U-Environment
M-Capabilities | Request-Action | Visual Object | Basic U-Location
M-Environment | Response-Action | Visual Basic Scene Descriptors | U-Location
M-Instance | Service Access | Visual Scene Descriptors | Finance
Program | Discover | Audio-Visual Object | Asset
Rights | Inform | Audio-Visual Basic Scene Descriptors | Provenance
Rules | Interpret | Audio-Visual Scene Descriptors | Transaction
Human and User |  | Audio-Visual Event Descriptors | Value
Account |  | Model | Wallet
Activity Data |  | Stream | 
Personal Profile |  | Summary | 
Personal Data |  | Universe-Metaverse Map | 

## Slide 37: MPAI-MMM – Technologies (MMM-TEC) V1.0
General | Process Interaction | Perception | Space
Contract | Message | Audio Object | Basic M-Location
E-Capabilities | P-Capabilities | Audio Basic Scene Descriptors | M-Location
Identifier | Process Action | Audio Scene Descriptors | U-Environment
M-Capabilities | Request-Action | Visual Object | Basic U-Location
M-Environment | Response-Action | Visual Basic Scene Descriptors | U-Location
M-Instance | Service Access | Visual Scene Descriptors | Finance
Program | Discover | Audio-Visual Object | Asset
Rights | Inform | Audio-Visual Basic Scene Descriptors | Provenance
Rules | Interpret | Audio-Visual Scene Descriptors | Transaction
Human and User |  | Audio-Visual Event Descriptors | Value
Account |  | Model | Wallet
Activity Data |  | Stream | 
Personal Profile |  | Summary | 
Personal Data |  | Universe-Metaverse Map | 

## Slide 38: Neural Network Watermarking (MPAI-NNW) V1.0
Neural Network Watermarking (MPAI-NNW) specifies methodologies to evaluate a neural network watermarking technology in terms of:
The impact on the performance of a watermarked neural network and/or on its inference.
The ability of a neural network watermarking detector/decoder to detect/decode a payload when the watermarked neural network has been modified.
The computational cost of injecting, detecting or decoding a payload in the watermarked neural network.

## Slide 39
User Agent
Communication
Global Storage
Controller
MPAI Store
Access
NNW
Decoder
Speech
Answer to Question Module
Image
Text
MPAI-AIF
Checker
Controller
User Agent
Proof
Watermark Provider
NNW
Decoder
Watermark Embedder
AIMs
Automatic Speech Recognition
End-user
Watermarking of generative AI
Text-To-Speech
Vocal answer
End-user
Text
WATERMARKED

## Slide 40: Neural Network Traceability (MPAI-NNT) V1.0
Technical Specification: Neural Network Traceability (MPAI-NNT) V1.0 specifies methods to evaluate aspects of Active (Watermarking) and Passive (Fingerprinting) Neural Network Traceability Methods:
Ability of a Neural Network Traceability Detector/Decoder to detect/decode/ match Traceability Data when the traced Neural Network has been modified.
Computational cost of injecting, extracting, detecting, decoding, or matching Traceability Data.
Specifically for active tracing methods, impact on the performance of a neural network with inserted Traceability Data and its inference.

## Slide 41: Portable Avatar Format (MPAI-PAF) V1.3
Specifies
  Portable Avatar and related Data Formats enabling a receiver to decode and render an Avatar in a Virtual Environment as intended by the sender.
  Personal Status Display Composite AI Module allowing the conversion of a Text and a Personal Status to a Portable Avatar.
  AI Workflows and AI Modules composing the Avatar-Based Videoconference Use Case also using Data Types from other MPAI Technical Specifications.
Portable Avatar Demultiplexing
Portable
Avatar
Avatar ID
Avatar
Avatar Space-Time
AV Scene Space-Time
Speech Object
Text Object
Language Selection
Personal Status
AV Scene Descriptors
Speech Model
Portable Avatar

## Slide 42: Avatar-Based Videoconference Use Case
Avatar Videoconference Server
Client Transmitter
Virtual Meeting Secretary
Input Selector
Avatar Model
Visual
Speech
Client Receiver
Output Audio
Output Visual
Summary
Summary
AV Scene
Descriptors
Spatial
Attitudes
Speech Object
Face Object
Portable Avatar
Portable Avatars
Portable VMS Avatar
Summary
Portable Avatars
Text
Output Text
Point of View

## Slide 43: Personal Status Display (PAF-PSD) V1.3
S
Machine Speech
Text-To-Speech
Entity Body Description
Portable Avatar Multiplexing
Portable Avatar
Machine Face Descriptors
Machine Body Descriptors
Machine Speech
Entity Face Description
Machine ID
Text Object
Speech Model
Personal Status
Text Object
PS-Face
PS-Speech
PS-Gesture
Text Object
Avatar Model
Avatar Model
Avatar Model
Personal Status Demultiplexing
Speech Model

## Slide 44: Object and Scene Description (MPAI-OSD) V1.2
Object and Scenes Description (MPAI-OSD) specifies
  Data Formats to describe uni- and multimodal Objects and Scenes, and their localisation in space.
  Basic and Composite AI Modules Visual Object Identification and Audio-Visual Alignment.
  AI Workflow: Television Media Analysis
Important Data Formats:
  Spatial Attitude, Time
  Audio, Visual, and Audio-Visual Object
  Audio, Visual, and Audio-Visual Scene Descriptors

## Slide 45: Television Media Analysis (OSD-TMA) V1.2
TV Splitter
User Agent
Audio-
Video-Text
Audio
Video
Audio-Visual Event Description
AV Event
Descriptors
Aut. Speech Recognition
Speech
Speech
Image
Time
Sp. Time
Speaker Time
Controller
Communication
Global Storage
MPAI Store
Access
AV Scene
Descrip.
Recognis.
Text
Speaker Time
Visual Change Detection
Speaker ID Recognition
Face ID Recognition
Speaker ID
Face ID(s)
Bounding
Box
Face Time
Speaker Time
Speaker ID
Aligned
Speaker ID
Aligned
Face ID
Audio-Visual Alignment
Face Time
Overlap
Overlap
Audio Segmentation
Aux. Text
Aux. Text
Auxiliary Text
Speech
Bounding
Box(es)
Audio-Visual Scene Description
Audio SA
Visual SA

## Slide 46: AI Module Profiles
AI Module Profiles (MPAI-PRF) specifies a label that uniquely identifies the set of AIM Attributes – input data, output data and functionality – that characterises an AI Module instance.
Attribute | Code
Text Object | TXO
Recognised Text | TXR
Object Instance ID | OII
Audio-Visual Scene Descriptors | AVS
Text Descriptors | TXD
Profile signalling | Comment
MMC-TST-V2.1(NUL+TXO@TRN#eng->ita) | Signals unsupported Attributes
MMC-TST-V2.1(ALL-ISD@TRN#kor<->fra#ger->swa) | Signals supported Attributes

## Slide 47: Data Types, Formats, and Attributes (MPAI-TFA) V1.2
AI Modules can process data better if they know better the data they process.
  A Visual Data Type instance can have different Sub-Types (colour space etc.)
  An Audio Data Type instance can have different content Format (MP3, AAC,…)
  A Speech Data Type instance can have different Attributes (to signal the language, the iD of the individual who generated the speech, etc.)
MPAI-TFA V1.0 defines JSON structures that convey information about Sub-Types, Formats, and Attributes of Media Types (e.g., Audio and Visual)
Currently, the following Data Types have Qualifier”: media, metaverse,and machine learning models.
MPAI digs deeply inside the nature of data….

## Slide 48: Being developed

## Slide 49: AI for Health (MPAI-AIH)
AI Health Platform composed of:
  End User Front Ends tasked with
    Acquiring and AI-based processing
    Licensing Health Data to Back End.
  A Back End tasked with
    Collecting and AI-based processing
    Enabling Third-Party Users to process licensed Health Data,
    Updating AI Models via federated learning techniques.
  A Blockchain tasked with managing Licences as Smart Contracts.
Licence formats
API
Taxonomy of AIH Processing functions
Data Formats

## Slide 50: Technical Specification: AI for Health (MPAI-AIH)
API
API
Data Storage & Access Services
Auditing Services
Authentication & Access Control Services
Blockchain and Distributed Ledger Technologies
Third-Party
Health-related
Entities
De-Identification & Anonymization Services
Global Secure Data Vault
Access to multiple services from smartphone (data storage, permissions, licenses, etc.)
Other sources
of health-
related data
Record of transactions on the B&DLT that can be used for audition purposes
Access to data (de-identified and anonym), processing of data through AI to extract knowledge
Licensing & Governance Services
AIH Federated
Learning System
User Agent
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
Controller
Global Storage
MPAI Store
Access
Communi-cation
Attestation Service
Encryption Service
Communication Service
AIM/AIW Storage
(non-secure)
AIM/AIW Storage
(secure)
User Agent
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
Controller
Global Storage
MPAI Store
Access
Communi-cation
Trusted Services
Attestation Service
Encryption Service
AIM Storage Service
Communication Service
AIM Security Engine
AIM Model Service
AIM/AIW Storage
(non-secure)
AIM/AIW Storage
(secure)

## Slide 51: End User Device
Specific Biometric
Sensors
Smartbands, Smartwatches, …
Biometric
Signals
End-user input data
AI-Health App
Secure Data Vault
Interaction
w/ Backend
Anomaly Detection & Risks Alert
Other installed health-related apps
User Agent
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
Controller
Global Storage
MPAI Store
Access
Communi-cation
Attestation Service
Encryption Service
Communication Service
AIM/AIW Storage
(non-secure)
AIM/AIW Storage
(secure)

## Slide 52: Server-based Predictive multiplayer Gaming (MPAI-SPG)
Technical Report: Guidelines for data loss mitigation in online multiplayer gaming provides guidelines on the design and use of neural networks to reliably and accurately predict missing players control data in an authoritative server context.
Context:
  In an online authoritative multiplayer game, each player uses a client to send control data to a server.
  The server updates the current game state with the data from all clients, and then broadcasts the updated game state to all clients.
  The data originating from a client may be properly or maliciously generated and properly received or not received.

## Slide 53: MPAI-SPG Reference Model
Behaviour Engine
Physics Engine
Rules Engine
Game State Engine
Online Game Server
Client 1
Client 2
Game State Engine- Mux
Controller
Communication
Global Storage
Game State Engine
- Dmux
Server-based Predictive
Multiplayer Gaming
Client N
MPAI Store
Behaviour Engine-AI
Rules
Engine-AI
Physics
Engine-AI

## Slide 54: Extended Reality Venues (MPAI-XRV) – Live Theatrical Stage Performance
Extended Reality Venues (MPAI-XRV) – Live Theatrical Performance defines interfaces of AI Modules (AIM) facilitating live multisensory immersive stage performances which ordinarily require extensive on-site show control staff to operate.
Goal: specify AIW, AIMs, and Data Types that enable
  Rapid mounting of a show in real and virtual venues.
  Orchestration of lighting, video, audio, and stage set cues adapted to live performers.
  Large shows to tour to smaller venues unable to support complex productions.
  Direct, precise yet spontaneous show implementation and control of multiple complex systems to achieve the show director’s vision.

## Slide 55: XR Venues- Live Theatrical Performance
Show Data
Performance
Descriptors
VE Action Descriptors
Virtual Env. Data
Operator Command
Interpretation
Participant Status Interpretation
Cue Point
Status
Participant
Status
Operator Status
Virtual Environment Experience Generation
Real Environment Experience Generation
Script
Controller
User Agent
Show Asset Repository (Global Storage)
Global Storage
MPAI Store
Access
Communi-cation
Attestation Service
Encryption Service
Communication Service
Performance Status Interpretation
Real Env. Data
RE Venue
Specification
VE Venue
Specification
Virtual
Environment
Real
Environment
Performance
Status
VE Venue
Specification
VE Command Data
VE Show Data
RE Venue
Specification
RE Command Data
RE Show Data
Real
Environment
Action Generation
VE Action Descriptors
Operator
Descriptors
Participant
Descriptors
Environment Description
Cue Point
Status
Cue Point
Status
Performance
Status
Participant
Status
Cue Point Identification
Cue Point
Status
Virtual
Environment
Operator Status
Show Data

## Slide 56: About to start

## Slide 57: AI-based End-to-End Video Coding (MPAI-EEV)/1
Compressed video representation that exploits AI-based end-to-end data coding technologies, i.e., without being constrained by how data coding has traditionally been applied in the of video coding context.
Goal: to achieve 20% performance improvement compared to VVC.

## Slide 58: AI-based End-to-End Video Coding (MPAI-EEV)/2

## Slide 59: Up-sampling Filter for Video applications (MPA-UFV)/1
BD-rate gain results (BD-PSNR, luminance)
Bicubic Down-sampling
Encoding
(EVC-VVC)
Decoding
(EVC-VVC)
Super Resolution Up-sampling
Error
EVC Baseline Profile | VVC Main 10 profile
HD24K: -7,44 | HD24K: -6,36
SD2HD: -21,62 | SD2HD: -26,05

## Slide 60: Up-sampling Filter for Video (MPA-UFV)/2
In Super Resolution with Intra Prediction, performance of EVC modified by enhancing/replacing existing coding tools with AI-based tools improves as in table.
Codec | Resolution | NN Intra Vs. Original Codec | Original Codec + SR Vs. Original Codec + bicubic | NN Intra + SR Vs. Original Codec + bicubic
EVC | SD2HD | -6.89% | -21,62% | -25,86%
EVC | HD24K | -6.89% | -7,44% | -11.99%

## Slide 61
We look forward to working
with you in MPAI on our workplan and your projects!
https://mpai.community/how-to-join/
61
61
61
61
Join MPAI
Share the fun
Build the future