## Slide 1: Technical Specification: Connected Autonomous Vehicle (MPAI-CAV) – Technologies (CAV-TEC) V1.0
Public online presentation
2025/05/08T15 UTC

## Slide 2: Connected and Autonomous Vehicles promise to
Save lives and reduce injuries (human errors replaced by less frequent machine errors).
Give humans more time for rewarding activities (e.g., interpersonal communication).
Optimise use of vehicles and infrastructure (“CAVs as a transport infrastructure used on demand”).
Reduce congestion and pollution (CAVs run only for a purpose).
Support elderly and disabled people.
Widely diffused CAVs will positively impact society and individuals.

## Slide 3: CAVs are important but the market is marginal?
It will take a long time for the CAV market to make a difference.
To positively impact society and individuals, today’s “niche market” must be transformed into tomorrow’s CAV “mass market” at an accelerated pace.
Standards are a faster and more efficient route to achieve a market of interchangeable components than waiting for market forces to produce more “monolithic” cars with progressively higher SAE Levels.
Early ‘900
Monolithic cars
Luxury market
Today Component cars
Mass market
Today Monolithic CAVs
Luxury market
Tomorrow Component CAVs
Mass market

## Slide 4: The standard Reference Model of Connected Autonomous Vehicle – Architecture (CAV-TEC V1.0)
CAV is partitioned into subsystems and components.
The Functional requirements of components are identified.
The formats of data exchanged by components are specified.
Environment Sensing Subsystem
(ESS)
Human-CAV Interaction
(HCI)
Autonomous Motion Subsystem (AMS)
Motion Actuation Subsystem
(MAS)

## Slide 5: Interface Standard life cycle
Specification of
  What the system does (“functional requirements”).
  The formats of the data exchanged through the interfaces.
Technological progress ïs not frozen.
A competitive market is enabled.
Independent developers offer competing but interchangeable components that perform better and better over time.
Eventually, an improved reference model will replace the current one with another, kicking off a new sequence of performance improvements.

## Slide 6: Benefits of an Interface Standard
  Researchers optimise component technologies.
  Component manufacturers bring their standard-conforming components to market once they are mature.
  Car manufacturers access an open global market of interchangeable components.
  Regulators oversee conformance testing of components following standard procedures.
  Users rely on Connected Autonomous Vehicles whose operation they can explain (to some extent).

## Slide 7: A CAV subsystem is not a black box
It could be designed as a black box
  Humans would have little knowledge and control of what happens inside.
MPAI has developed the AI Framework standard (MPAI-AIF)
  Specifies a set of standard APIs enabling access to system functionalities.
  Supporting systems – called AI Workflows
  Made of components – called AI Modules
    Specified by function and interfaces, not by implementation.
    Instances can be replaced by instances of a different make.
  MPAI-AIF enables a component-based specification.

## Slide 8: AI Framework (MPAI-AIF)
User Agent
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
AI Module (AIM)
Controller (Non-secure/Secure)
Global Storage
MPAI Store
Access
Inputs
Outputs
Communi-cation
AIM/AIW Storage
(non-secure)
AIM/AIW Storage
(secure)
SAL
Attestation Service
Encryption Service
Communication Service

## Slide 9: Human-CAV Interaction (HCI) Functional Requirements
Recognises human owner or renter (physically present or remote).
Responds to humans’ commands and queries.
Converses with humans.
Manifests itself as a perceptible entity (avatar).
Exchanges information with the Autonomous Motion Subsystem in response to humans’ requests, e.g., passenger wants to:
  Stop for errands.
  See & hear the world perceived by CAV (Full Environment Descriptors - FED).
Communicates with HCIs of other CAVs.

## Slide 10: Reference Model: Human-CAV interaction (CAV-HCI)
Aut. Speech Recognition
Face Descriptors
Body Descriptors
Speech Object
Speech
Object
Speech Object
Face Object
Face ID Recognition
Face ID
Entity Dialogue Processing
Speaker ID Recognition
Speaker ID
Machine Text
Personal Status Display
Machine
Personal Status
Recognised Text
Personal Status
Visual Object Identification
NLU Text
User Agent
Autonomous Motion
Subsystem
Point of View
Machine Portable
Avatar
Meaning
Controller
Global Storage
Access
Communication
Attestation Service
Encryption Service
Communication Service
MPAI Store
Environment Sensing Subsystem
Participant IDs
Meaning
Input Visual
AV Scene Descriptors
Audio=-Visual Scene Rendering
Output Text
AV Scene Descriptors
Visual Object ID
Natural Language Understanding
Visual Scene
Descriptors
Output Visual
Output Audio
Autonomous Motion Subsystem
AMS-HCI
Message
Remote HCIs
Ego-Remote HCI Message
Input Audio
Input Text
Participant
IDs
Visual Scene Descriptors
Visual
Object ID
Personal Status Extraction
Speech Scene Geometry
Visual Scene Geometry
Output Speech
Audio-Visual Scene Description

## Slide 11: What does CAV-HCI specify?
HCI Subsystem
  I/O data
  Functional Requirements
  Components’ functions and topology
Input data
  Audio, Text, Visual
  Point of View
  Audio-Visual Scene Descriptors
Output data
  Audio, Speech, Text, Visual
  Ego-Remote HCI Messaging
  AMS-HCI Messaging

## Slide 12: HCI input data
Input data | From | Description
Point of View | Passenger | Passenger's Point of View looking at environment.
Audio-Visual Scene Descriptors | AMS Subsystem | Audio-Visual representation of the environment.
Input Audio | Environment, Passenger Cabin | User authentication, command/interaction with HCI, etc. and environment Audio.
Input Text | User | Text complementing/replacing User input
Input Visual | Environment, Passenger Cabin | Environment perception, User authentication, command/ interaction with HCI, etc. and environment Visual.
AMS-HCI Message | AMS Subsystem | AMS response to HCI request.
Ego-Remote HCI Message | Remote HCI | Remote HCI to Ego HCI.

## Slide 13: HCI output data
Output data | To | Description
Output Audio | Cabin Passengers | HCI’s avatar or FED Audio.
Output Speech | Cabin Passengers | HCT's avatar Speech.
Output Text | Cabin Passengers | HCI’s avatar Text.
Output Visual | Cabin Passengers | HCI’s avatar or FED Visual.
AMS-HCI Message | AMS Subsystem | HCI request to AMS, e.g., Route or Point of View.
Ego-Remote HCI Message | Remote HCI | Ego HCI to Remote HCI.

## Slide 14: Components/1
AIM | Function
Audio-Visual Scene Description | 1. Receives Audio and Visual Objects from the appropriate Devices. 2. Produces Audio-Visual Scene Descriptors.
Automatic Speech Recognition | 1. Receives Speech Objects. 2. Produces Recognised Text.
Visual Object Identification | 1. Receives Visual Scenes Descriptors. 2. Provides Instance ID of indicated Visual Object.
Natural Language Understanding | 1. Receives Recognised Text. 2. Uses context information (e.g., Instance ID of object). 3. Produces Meaning & Natural Language Understanding Text, using Refined or Input.
Speaker Identity Recognition | 1. Receives Speech Object of a human and Speech Scene Geometry. 2. Produces Speaker ID.

## Slide 15: Components/2
AIM | Function
Personal Status Extraction | 1. Receives Speech Object, Meaning, Face Descriptors and Body Descriptors of a human with a Participant ID. 2. Produces the human's Personal Status.
Face Identity Recognition | 1. Receives Face Object of a human and Visual Scene Geometry. 2. Produces Face ID.
Entity Dialogue Processing | 1. Receives Speaker ID, Face ID, AV Scene Descriptors, Meaning, Natural Language Understanding Text , Visual Object ID, and Personal Status. Moreover, it receives AMS-HCI Messages and Ego-Remote HCI Messages. 2. Produces Machine (HCI) Text Object and Personal Status. Moreover it produces AMS-HCI Messages and Ego-Remote HCI Messages.
Personal Status Display | 1. Receives Machine Text Object and Machine Personal Status. 2. Produces Machine’s Portable Avatar.
Audio-Visual Scene Rendering | 1. Receives AV Scene Descriptors, Portable Avatar, and Point of View. 2. Produces Output Speech, Output Audio, and Output Visual.

## Slide 16: AI Modules/1
AIM | Input | Output
Audio-Visual Scene Description | - Input Audio - Input Visual | - AV Scene Descriptors
Automatic Speech Recognition | - Speech Object | - Recognised Text
Visual Object Identification | - AV Scene Descriptors - Visual Objects | - Visual Object Instance ID
Natural Language Understanding | - Recognised Text - AV Scene Descriptors - Visual Object Instance ID - Input Text | - NLU Text - Meaning
Speaker Identity Recognition | - Speech Object - Speech Scene Geometry | - Speaker ID
Personal Status Extraction | - Meaning - Input Speech - Face Descriptors - Body Descriptors | - Personal Status

## Slide 17: AI Modules /2
AIM | Input | Output
Face Identity Recognition | - Face Object - Visual Scene Geometry | - Face ID
Entity Dialogue Processing | - Ego-Remote HCI Message - AMS-HCI Message - Speaker ID - Face ID - Meaning - NLU Text - Visual Object Instance ID - Personal Status | - Ego-Remote HCI Message - AMS-HCI Message - Machine Text - Machine Personal Status
Personal Status Display | - Machine Personal Status - Machine Text | - Machine Portable Avatar
Audio-Visual Scene Rendering | - AV Scene Descriptors - Machine Portable Avatar - Point of View | - Output Text - Output Speech - Output Audio - Output Visual

## Slide 18: Data Types of CAV-HCI
3D Model Object | Orientation
AMS-HCI Message | Perceptible Entity
Annotation | Personal Preferences
Audio Object | Personal Profile
AV Scene Descriptors | Personal Status
Body Descriptors | Portable Avatar
Ego-Remote HCI Message | Speech Object
Face Descriptors | Text Object
Instance Identifier | Visual Object
Meaning | 

## Slide 19: The blessing – and curse – of formats
Formats represent a particular type of data.
  3D graphics, Audio, Visual, and a lot more …
A machine can understand data, if it knows how to interpret it.
A functionality depends on data type, much less on the format used.
CAV-TEC mostly specifies data types, not formats.
Qualifiers convey information about the features of a data type.
E.g., a Visual Data Type instance:
  Uses a given colour space (Sub-Type).
  Was produced by an AVC encoder and streamed with DASH (Format).
  Is described by Dublin Core Metadata (Attribute).

## Slide 20: The Environment Sensing Subsystem (CAV-ESS)
CAV-ESS acts as the CAV’s eyes, ears (and as a few more senses).
A CAV represents its environment using various specific Environment Sensing Technologies (EST) sharing the same Scene Representation Format.
The Basic Environment Description AIM integrates all EST-specific Object-based Scene Representations to produce Basic Environment Descriptors.
If an EST-specific AIM discovers a suspect object, it immediately sends an Alert to the Autonomous Motion Subsystem.
LiDAR Scene Descriptors
LiDAR Scene Description
Spatial Attitude
LiDAR Object
Other Scene Descriptors
Alert

## Slide 21: Reference Model: Environment Sensing Subsystem
OfflineMap Scene Description
Ultrasound Scene Description
LiDAR Scene Description
RADAR Scene Description
Visual Scene Description
Spatial Attitude Generation
Audio Scene Description
Autonomous Motion Subsystem
Basic Env. Descriprors
Alert
Motion Actuation Subsystem
Spatial Attitude
GNSS Object
Spatial
Attitude
Audio Object
Audio Scene Descriptors
Alert
Basic Environment Descriptors
Visual Scene Descriptors
Alert
Basic Environment Descriptors
RADAR Scene Descriptors
Alert
Basic Environment Descriptors
LiDAR Scene Descriptors
Alert
Basic Environment Descriptors
Ultrasound Scene Descriptors
Alert
Basic Environment Descriptors
Offline Map Scene Descriptors
Weather Data
Visual Object
RADAR Object
LiDAR Object
Ultrasound Object
Offline Map Object
Controller
Global Storage
Access
Communi-cation
Attestation
Service
Encryption
Service
Communication
Service
MPAI Store
Alert
Alert
Alert
Alert
Basic Environment Description
Full Env. Descriprors

## Slide 22: The data types of CAV-ESS
Alert | Offline Map Object | Space-Time
Basic Environment Descriptors | Offline Map Scene Descriptors | Spatial Attitude
Bounding Box | Path | Time
Coordinates | Point of View | Traffic Rules
GNSS Object | Position | Traffic Sign Objects
LiDAR Object | RADAR Object | Trajectory
LiDAR Scene Descriptors | RADAR Scene Descriptors | Ultrasound Object
Location | Road State | Ultrasound Scene Descriptors

## Slide 23: Reference Model: Autonomous Motion Subsystem
FED
Route
Controller
Global Storage
Access
Communication
Attestation
Service
Encryption
Service
Communication
Service
MPAI Store
Environment Sensing Subsystem
Remote AMSs
AMS-MAS msg
Alert
Full Environ.
Descriptors
AMS Data
Road &
CAV State
AMS
MAS msg
Motion Actuation Subsystem
Human-CAV Interaction
Basic Environ.
Descriptors
AMS-HCI
Message
User Agent
Environment Sensing Subsystem
Alert
Full Environ.
Descriptors
AMS
Data
FED
AMS
Data
Road &
CAV State
AMS
Data
AMS
Data
FED
FED
FED
Route
Path
Motion Selection Planning
Traffic Obstacle Avoidance
Route Selection Planning
Trajectory
Path Selection Planning
Path
AMS
Data
AMS-MAS msg
Full Environment Description
AMS Memory
Trajectory
FED
Request
Req.
Request

## Slide 24: CAV-AMS Data Types
AMS-MAS Message | Ego-Remote AMS Message
AMS Data | Full Environment Descriptors
CAV Identifier | Road Attributes
CAV State | Route

## Slide 25: An example of AIM integration: Trajectory Planning and Decision AIM
Route
Path
Path Selection Planning
FED
Traffic Obstacle Avoidance
Trajectory
FED
Alert
Alert
AMS
Data
AMS-MAS Message
Motion Selection Planning
AMS-MAS Message
Road State
CAV State
Request
Request
Request

## Slide 26: An example of CAV-TEC data type specification Ego-Remote AMS Message/1
Label | Size | Description
Header | N1 Bytes | Ego-Remote AMS Message Header
- Standard-EgoRemoteAMSMessage | 9 Bytes | The characters “MMM-ERA-V”
- Version | N2 Bytes | Major version – 1 or 2 Bytes
- Dot-separator | 1 Byte | The character “.”
- Subversion | N3 Bytes | Minor version – 1 or 2 Bytes
EgoRemoteAMSMessageID | N4 Bytes | Identifier of Ego-Remote-AMS Message.
RequestMessage | N5 Bytes | CAV's Request
- EgoCAVID | N6 Bytes | CAV ID
- ULocation | N7 Bytes | Specification of Remote CAV's Environment portion.
ResponseMessage | N8 Bytes | Data of Ego-Remote-AMS Message
- RemoteCAVID | N9 Bytes | M-Location in Remote AMS.
- RemoteFED | N10 Bytes | Subset of FED relevant to requested U-Location.

## Slide 27: An example of CAV-TEC data type specification Ego-Remote AMS Message/2
Label | Size | Description
SenderInfoMessage | N11 Bytes | Message sent for information
- EgoCAVID | N12 Bytes | CAV ID
- Trajectory | N13 Bytes | Trajectory Ego AMS intends to adopt.
ReceiverInfoMessage | N14 Bytes | Message sent for information
- EgoCAVID | N15 Bytes | CAV ID
- Accept/Reject | N16 Bytes | Trajectory accepted/rejected by receiving Remote AMS
AMSAlertMessage | N17 Bytes | Messages alerting CAVs about Ego CAV status.
- EgoCAVID | N18 Bytes | CAV ID.
- AMSAlertMessage | N19 Bytes | One of Ambulance, Authority, Health, Evacuation Messages.
- Road State | N20 Bytes | Appropriate subset of Road State.
- CAV State | N21 Bytes | Appropriate subset of CAV State.
DescrMetadata | N22 Bytes | Descriptive Metadata

## Slide 28: An example of CAV-TEC data type specification Ego-Remote AMS Message/3
https://schemas.mpai.community/CAV2/V1.0/data/EgoRemoteAMSMessage.json

## Slide 29: Reference Model: Motion Actuation Subsystem
Autonomous Motion Subsystem
(AMS)
Spatial Data
Weather Data
Environment Sensing Subsystem (ESS)
Spatial Attitude
User Agent
Controller
Global Storage
Access
Communication
Attestation Service
Encryption Service
Communication Service
MPAI Store
MAS Spatial Attitude Generation
Ice Condition Analysis
Brake response
Motor response
Wheel response
Weather Data
Spatial
Attitude
Brake response
AMS-MAS Message
Brake command
Motor command
Wheel command
AMS-MAS Message
AMS-MAS Message Interpretation
MAS Response Analysis
Motor response
Wheel response
Road State

## Slide 30: CAV-TEC V1.0 – an example of MPAI-wide collaboration
AI Framework | AI Framework applied to subsystems and underlying Security Abstraction Layer.
Context-based Audio Enhancement | Audio-related technologies.
Object and Scene Description | 3D Model, Audio, Audio-Visual, LiDAR, Offline Map, RADAR, Speech, Ultrasound, and Visual Object and Scene Descriptors.
Multimodal Conversation | Technologies enabling a human to converse with a machine.
Portable Avatar | 3D Graphics-related technologies.
MPAI Metaverse Model | Full Environment Descriptors.
Data Types, Formats, and Attributes | Qualifier support to CAV data.

## Slide 31: CAV-TEC V1.0 is a stepping stone…
From the capabilities of the CAV specified by CAV-TEC V1.0:
  Interact with humans
  Perceive the environment
  Create a model of the environment by collaboration
  Move the CAV around to reach a destination.
To a CAV that is:
  A full element of the Internet of Vehicles.
  Interacting with various services.
  Implemented as running (open-source software).

## Slide 32
We look forward to working
with you
on this exciting MPAI project!
https://cav.mpai.community/
32
32
32
32
Join MPAI
Share the fun
Build the future